GreatSim Works

Machining Simulation Lathe User Manual

More video tutorials on http://www.greatsim.com/Support

1.Getting Started:

Right Mouse Button Menu:

- A. Panel XOZ :Change view

- B. Panel YOZ :Change view

- C. Panel XOY :Change view

- D. Hide/Show machine body:

To hide/show machine body , select "Hide body" or "Show body" .

- E. Move to center:

Move to the center of workpiece immediately .

F. Open/Close door

To open/close door , release Emergency button and power on , then select "Open door" or "Close door" .

Transform machine model:

A. To rotate machine model , click left mouse button and drag it .

B. To zoom in and out machine model ,roll mouse wheel to zoom .

C. To pan machine model , press mouse wheel and drag with it to pan .

Tips for transforms:

Main menu

- A. Estimate time

Estimate CNC machining time for a CNC program .

- B. FIle

1.Import : Import a CNC program under which EDIT mode is available and a CNC file is opened or created .

2.Save workpiece : Save machined workpiece .

3.Read workpiece : Read saved workpiece .

- C. Settings

1.Displaying programming trace:

When on , show programming trace during auto run . When off , hide programming  trace.

2.Display body:

When on , show body , when off ,hode body.

3. Sound effect:

When on , enable sound , when off , disable sound .

4. Shadow effect:

When on , enable shadow effect , when off , disable shadow effect . If some obsolete display adapters cause several types of problems , such as running slowly , the option better be disabled .

- D. View

1.View panels : When CNC panel is closed , use the menu to reopen CNC panel .

2.Show in dual monitors : Separately show panels and 3D model in dual monitors .

- E. Switch panel

Switch CNC system to one another .

- F. Workpiece

Select type of workpiece , workpiece types : box and cylinder . Improve the smoothness of workpiece you can see on the screen :

1. Performance : Jaggies
      2. Balance : Less jaggies
      3. Quality : Smooth , you will experience a decrease in performance with the high value .

It is recommended to select a value based on how your display adapter can perform .

- G.Check for updates

Check if a newer version .

- G. Help

2. Tool select

Click the left tool icon in the machine view, the Tool library dialog pops up. A tool list on the left side displaying all tools , another list on the right side displaying the tools on turret. The parameters of tool and insert are shown below.

- Add a tool:

Enter new parameters for a new tool and then press “Add” button.

2 . Modify :

Click an item in the tool list , the selected tool’s parameters will be shown below, modify them and then press “Modify” button.

3 . Delete:

Click an item in the tool list and then press “Delete” button, the selected tool will be deleted.

4 . Mount tool:

Right Click an item in the tool list or press “Mount to>>” button after clicking an item in the tool list, the menu showing the turret station number will pop up, select a station where a tool will be mounted.

Click an item in the turret list, press “Tool ready” , the turret will rotate and index the selected station to the machining position .

3. CNC Panel

FANUC 0iM Control panel

Emergency button

Power on

Power off

Cycle start

Cycle stop

Auto Edit MDI INC

Handle REF Jog

Coolant

Main spindle CW,Stop,CCW

Rapid

Rate for INC mode :0.001 , 0.01 , 0.1 , 1.0

Main spindle override

Feedrate override

Program protect

A. Edit program

PressEdit button and then  PROG button on system panel , select "DIR" , as following :

- 1. Open a CNC program : Enter a CNC program name that exsits in the system , such as "O0001" , press ArrowDown button on system panel  to open it .

- 2. Create a CNC program : Enter a CNC program name that doesn't exist in the system , such as "O0001" , press "Insert" button . Program protect  must be unlocked before creating a new CNC program .

- 3. Edit a CNC program :

Use the three buttons  to edit a program : Alter , Insert , Delete . Edit is not available until program protect is unlocked .

- 4.Delete a CNC program : Enter a CNC program name , press "Delete" button .

- 5.Import a CNC program from your disk:

  - Switch to EDIT mode in the Simulation , and then either create or open a CNC program .

  - New a Notepad text file .

  - Enter or paste CNC program into the text file .

  - Select "Save as" and select "Save as type:" as "All files" .

  - Enter a file name , such as "XXXX.cnc" or "XXXX.nc" .

  - Use Import  menu in the Simulation to select the file , click "Open" .

  - The file is imported.

B. Auto run

Open , create or import a CNC program , press , then press Cycle start .

Press  to enable Single Block . When on , CNC program will be executed in a single block , when off , the function is disabled .

C. Offset input

Select edge finer from left tool bar and mount it to main spindle .

Use Right Button menu to select Panel XOZ , press to approach slowly to the edge of workpiece until LED is on , as following:

1．Offset

Moving mouse onto tool shank ,the tool information will be shown，and then right-click on the tool shank to pop up the menu as below:

Select “Tool ready” , the turret will index the station to the machining position.

Right-click on the machine view to pop up the menu , select “Move to center” ,the tool nose aligns with the center of work piece.

Press “OFFSET SETTING”,an image shown as below:

Press “OFFSET” soft key，enter “X0”，press “Measure” soft key, offset for X is done, Z axis is the same as X.

2．G54-G59

Select "Work" , an image shown as following:

UseArrow button to select G54 , enter X50 , select "Measure"  .

Steps for Y axis is similar to steps for X axis .

Steps for Z axis : Mount a tool on main spindle , approach to the surface of workpiece slowly and cut it slightly , enter "Z0" , select "Measure" . For more information ,download :the video tutorial on http://www.greatsim.com/Support/presettool.rar

D. MDI

Pressbutton , pressbutton , an image shown as following：

Select "MDI" , enter a block , such as "G54X0Y0Z0" , press to execute the block you enter .

4.Use Hand Wheel

To use Hand Wheel , Double Click on Hand Wheel . To close Hand Wheel , Double Click on it again.

5.Note

If there is a problem with displaying 3D model , please make sure the hardware accelerations are enabled before running the application .

GreatSim Works
 http://www.greatsim.com
feedback@greatsim.com